## Slide 1: Enhanced LLM-aided Testbench Generation
Automated Verilog Testbench Generation with Golden Reference Models

## Slide 2: Project Overview
🎯 Automated testbench generation for Verilog modules
🤖 Leverages Large Language Models (LLMs) for intelligent code generation
✅ Creates comprehensive test patterns with verification logic
🔍 Generates Python golden reference models for expected outputs
⚡ Streamlines hardware verification workflow
Key Benefits:
  Reduces manual testbench writing effort
  Ensures comprehensive test coverage
  Provides automatic pass/fail verification

## Slide 3: Testbench Generation Framework: Inputs & Outputs
📥 INPUTS:
  Natural Language Description
    Text file describing module functionality
    Input/output specifications
    Expected behavior details
  Verilog Module Code
    The actual HDL implementation to be tested
    May contain bugs to be detected
📤 OUTPUTS:
  testbench_initial.v - Testbench with test patterns
  golden_model.py - Python reference implementation
  test_patterns_with_golden.json - Test data with expected outputs
  testbench_final.v - Complete testbench with verification logic

## Slide 4
5-Step Pipeline Workflow
Step 1-2: Input Handling
Natural Language Description + Verilog Code
Step 3: LLM Testbench Generation
Generate comprehensive test patterns
Step 4: Golden Model Generation
Python model + Expected outputs
Step 5: Testbench Update
Add verification logic & assertions
✅ Final Testbench Ready

## Slide 5: Example: 2-to-1 Multiplexer

## Slide 6: Example: 2-to-1 Multiplexer

## Slide 7: Step 3: LLM-Powered Testbench Generation
📝 Process:
  Extracts module information (name, inputs, outputs)
  LLM generates comprehensive test patterns covering:
    Corner cases (all 0s, all 1s)
    Boundary values
    Typical use cases
    Random test patterns
  Creates Verilog testbench skeleton
📄 Output: testbench_initial.v
  Signal declarations
  Module instantiation
  Test pattern application
  Basic $display statements
  ⚠️ Does NOT contain expected outputs yet

## Slide 8: Testbench Generation Prompt

## Slide 9: Testbench Generation Prompt

## Slide 10: Step 4: Golden Model Generation
🐍 Python Golden Reference Model:
  LLM converts natural language description to Python code
  Implements expected module functionality
  Independent verification reference
🔄 Golden Output Computation:
  All test patterns executed through Python model
  Expected outputs computed and saved
  Results stored in JSON format
📄 Outputs:
  golden_model.py - Python implementation
  test_patterns_with_golden.json - Test data with expected results

## Slide 11: Golden Python Model Generation Prompt

## Slide 12: Step 5: Testbench Enhancement with Verification
✨ Testbench Enhancement:
  Adds verification logic for each test case
  Injects expected outputs from golden model
  Implements pass/fail tracking
  Generates comprehensive test summary
✅ Verification Features:
  Automatic comparison of actual vs expected outputs
  Detailed error reporting for failures
  Test statistics (total, passed, failed)
  Color-coded output for easy debugging
📄 Output: testbench_final.v
  Production-ready testbench with full verification

## Slide 13: Testbench Enhancement Prompt

## Slide 14: Testbench Enhancement Prompt

## Slide 15
Iverilog-based Evaluation Framework
Verilog Module (Design Under Test)
testbench_final.v (Generated Testbench)
iverilog Compiler
sim.vvp (Compiled Binary)
vvp Simulator
📊 Simulation Results Test Summary (Pass/Fail)

## Slide 16: Conclusion
🎉 LLM-aided Testbench Generation provides:
  ✅ Complete automation of testbench creation
  ✅ Comprehensive test coverage with minimal effort
  ✅ Golden reference models for verification
  ✅ Integration with standard simulation tools (iverilog)
  ✅ Significant time savings in hardware verification
🚀 Future Enhancements:
  Support for sequential circuits and FSMs
  Waveform generation and analysis
  Coverage analysis and reporting
  Integration with formal verification tools
📧 GitHub: https://github.com/FCHXWH823/LLM-aided-Testbench-Generation.git